DRAFT

OIL FINISHING PROCESS

MINWAX WIPE-ON POLY AND MINWAX TUNG OIL

1. Sand the turning, removing all sanding marks or blemishes to 320 grit or better. Finishing will only make sanding errors more prominent.  Remove all dust.

2. With the work piece stationary or turning slowly, wipe on a full wet coat of Minwax Wipe-on Poly clear gloss  finish.  Let the finish soak into the piece for a few minutes. If dull spots appear in the coating as the finish is soaking into the wood, apply more finish to the area. While the finish is still wet, wipe the piece dry with a clean cotton cloth, then buff dry with the lathe running.

3. Set the turning aside for at least two to three hours or preferably overnight.

4. Sand lightly with you final grit paper or 0000 steel wool to remove any finish left on the surface.  A second coat of finish may be considered.

5. Place Minwax Tung Oil on a pad of 0000 steel wool. With the piece spinning on the lathe, apply the steel wool and oil to the turning. The steel wool buffs the surface of the wood, and the oil restores the sheen.  Buff the piece with a soft cloth. Set aside overnight to dry.

6. Repeat the oil, steel wool and buffing process until satisfied with the finish.

7. Remove the turning from the faceplate and treat the piece with coats of oil, buffing dry between each coat until the desired appearance is achieved.

DRAFT

MT. DIABLO TURNING CENTER

STANDARD FINISHING METHODS

1.	Mahoney's Finishing Oil

- Walnut Oil and Bees Wax

- Used for utilitarian turned pieces

- Low sheen

- Absolutely food safe

- Easily renewable

2.	Minwax Wipe-on Ploy/Minwax Tung Oil

- Polyurethane and natural Tung oil with additives

- Used for high/medium gloss finished turned pieces

- Considered food safe

3.	CA Finish

- CA Glue finish

- Used for pens or other turned pieces requiring a hard/high gloss finish

- High Gloss/durable