Turning Your First Platter

Here is one way to turn a platter using the minimum of lathe fixtures & accessories:

- Prepare a face plate and glue block

  - Make the glue block dead flat and sanded

- Cut blank of one inch thick stock to fit your lathe

  - Mark the center on both sides

  - Remove the corners

  - Sand face side dead flat for gluing

- Glue face side of blank to the glue block

  - Use the tail stock for alignment

- Using a deep-fluted gouge, carefully round the edge of the blank

- Flatten face and back of blank with deep-fluted gouge

- Lay out project

  - Mark depth of rim, bowl and foot on edge of blank

  - Mark diameter of foot on base side

  - Mark diameter of recess for selected chuck

- Cut recess to fit selected chuck’s expanding jaws

  - Be sure recess is not more than 1/8 inch deep

  - Recess must be shaped to match the expanding chuck jaws

  - Sand the recess interior to completion

- Turn bottom of bowl and rim sections

  - Complete and sand

- Shape edge of platter interior

  - Complete the interior of the rim

  - Sand to completion

- Reduce interior of bowl area to near the glue block if possible

  - Watch thicknesses carefully

- Reverse platter into the expanding chuck

  - Do not over tighten jaws

- Remove faceplate carefully

  - Reposition tailstock to support project

- Reduce glue block to approximately ½ inch

- Reduce interior carefully

  - Constantly check thickness of bowl area

- Level out interior

  - Completely remove glue block remnant

  - Complete interior

  - Check flatness with a straight edge

- Sand and complete interior

  - Add finish

- Reverse and complete the base

  - Using “jumbo jaws” with your chuck

  - Using a jam chuck with rubber pad

    - Remove point from live center and add a hard rubber block

    - Readjust platter position to center perfectly and tighten the tailstock

    - Remove excess stock from base, sand, finish

Here are some videos that may also be helpful:

http://www.woodturningonline.com/Turning/Projects/plates.html

http://www.youtube.com/watch?v=ip0ThPqIgJY&feature=related

http://www.youtube.com/watch?v=udj9euwBEVE&feature=related